## Slide 1: Detector Response Modeling: Dual Aperture X-ray Solar Spectrometer
APPM 4380
Final Project
Robert Sewell

## Slide 2: Outline
Motivation
Design
Response
Spectra

## Slide 3: Motivation
Miniature X-ray Solar Spectrometer (MinXSS-1) CubeSat measured the soft X-ray spectra using the Amptek X123 X-ray spectrometer
  0.5-30keV photon energies, gap in the solar spectra
  Single beryllium aperture - reduced field of view to limit
  saturation during flare events
Dual Aperture X-ray Solar Spectrometer (DAXSS) allows for
higher energy counts
  Increase field of view, add a thin filter to attenuate lower
  energy photons
  Difficult to model response - interplay between the two
  filters

## Slide 4: Design
Kapton-25micron, Pinhole Diameter-0.81mm
Tungsten cover with aperture opening to Kapton filter with a pinhole to the exposed beryllium
Need to model possible filter materials and aperture diameters
  Material should not have a k-edge
  near 0.5keV-3keV – choose
  carbon based material
  (Kapton – C22N2O4H12)
Model detector response using
example solar flux (quiet to average
solar spectra)
  Henke model of x-ray
  transmission
  S(E)=Fsolar(E)Tboth(E)
Notes: Kapton,mylar,lexan all nearly have same transmission profile

## Slide 5: Detector Response Model
Discrete bins blend sum over continuum of photon energies – model bin width FWHM
Calibrate with known source (Synchrotron Ultraviolet Radiation Facility) to model best fit of beryllium and Kapton thicknesses
  S(E)=∑[TBEFsmall+TbothFlarge]*Gaussian(FWHM)*(Bin Width)
  Transmission of beryllium and Kapton are variable with thicknesses

## Slide 6: Nelder-Mead Minimization
Minimize χ2 error between model response and calibration response
Use nelder-mead method with a simplex in Kapton-beryllium thickness space
Iterate with different simplexes to verify global minima

## Slide 7: Hybrid Model – Full Spectra
Henke transmission model works well for Ephoton>1keV to provide a continuum
  Photon-electron effects prevalent <1keV
  Direct inversion at middle beam energy as an approximation

## Slide 8: Launch
DAXSS launched on NASA Sounding rocket 36.336
  Calibration mission for SDO EVE
  Secondary payload (12 instruments total)
White Sands Missile Range, New Mexico –
2018-06-18 19:00:00 UTC

## Slide 9: Launch

## Slide 10: Spectral Fitting
CHIANTI spectra modeling to fit rocket flight data using detector response matrix model
  Several tunable parameters (two temperature fits, elemental abundances)
  Minimize χ2 with similar method in n-dimension parameter space
  Need to implement Nelder-Mead or similar minimization algorithm as binary search is computationally expensive

## Slide 11: Future Directions
Photo-electron effects
Nelder-mead for spectral fitting
Feasibility for CubeSat mission

## Slide 12: Works Cited
Bradt, Hale. Astronomy Methods: a Physical Approach to Astronomical Observations. Cambridge University Press, 2009.
Caspi, Amir, et al. “New Observations Of The Solar 0.5–5 Kev Soft X-Ray Spectrum.” The Astrophysical Journal, vol. 802, no. 1, 2015, doi:10.1088/2041-8205/802/1/l2.
Joglekar, Sachin. “Nelder-Mead Optimization.” Sachin Joglekar's Blog, 16 Jan. 2016, codesachin.wordpress.com/2016/01/16/nelder-mead-optimization/.
http://jsoc.stanford.edu/images/fixed/AIA_131.jpg